## Slide 1
Welcome to the Lecture
on
Basic Mechanical Engineering Drawing
(ME 1270)
Tashin Ahmed Apon
Lecturer (Full-Time Adjunct)
Department of Mechanical Engineering
Bangladesh Army University of Engineering & Technology
RUET, Bangladesh
All Praises and Glory be to ALLAH
Bangladesh Army University of Engineering & Technology

## Slide 2: Outlines
Engineering Drawing Definition and Function
Standard
Line Types and Styles
Letters and Numbers
Scale
Paper Size
Drawing Title

## Slide 3: What is Engineering Drawing?
Department of Mechanical Engineering, RUET
Drawing—a graphical language that communicates ideas and information from one mind to another without the barrier of a language
A picture/drawing is worth a thousand words
Drawings are the road maps which show how to manufacture products and structures

## Slide 4: What is Engineering Drawing?
Engineering drawing – A drawing of an object that contains all information, like actual shape, accurate size, manufacturing methods, etc., required for its construction
Most especially, it communicates all needed information from the engineer who designed a part to the workers who will make it.

## Slide 5: Engineering Drawing Function
Information delivery
Preservation, archiving, use of information
Ways of thinking in the preparation of information

## Slide 6: Some Examples of Engineering Drawing
Department of Mechanical Engineering, BAUET

## Slide 7: Some Examples of Engineering Drawing...
Department of Mechanical Engineering, BAUET

## Slide 8: Some Examples of Engineering Drawing...
Department of Mechanical Engineering, BAUET

## Slide 9: Some Examples of Engineering Drawing...
Department of Mechanical Engineering, BAUET

## Slide 10: Engineering Drawing Function
Department of Mechanical Engineering, BAUET
Drawings convey the following critical information:
Geometry – the shape of the object; represented as views; how the object will look when it is viewed from various angles, such as front, top, side, and so on.
Dimensions – the size of the object is captured in accepted units.
Tolerances – the allowable variations from the nominal size for each dimension.
Material – represents what the item is made of.
Finish – specifies the surface quality of the item, functional or cosmetic.

## Slide 11: Types of Drawing
Department of Mechanical Engineering, BAUET
Engineering drawing is completely different from artistic drawing, which are used to express aesthetic, philosophical, and abstract ideas.
Nature
Drawing
(Scenery)
Geographical
Drawing (Maps)
Botanical
Drawing
(Flower, Plant)
Zoological
Drawing
(Creatures, animals)
Portraits
(Human Face,
expressions)
Engineering
Drawings
Building Related Drawing
Machine component Drawing
Orthographic
Projection
Isometric
Projection

## Slide 12: Types of Drawing…
Department of Mechanical Engineering, RUET
Computer has a major impact on the methods used to design and create technical drawings.
Design and drafting on computer are cheap and less time consuming.
Why we go for manual drawing?
Engineering Drawing
Manual Drawing
CADD

## Slide 13: Why we go for manual drawing?
Department of Mechanical Engineering, BAUET
Computer cannot replace the drafting board and equipment as a learning tool
If basic fundamentals are clear, better use can be made of the power of the software
To be an expert in technical drawing, this first course on Engineering (manual) Drawing is the first step

## Slide 14: Items required for drawing
Department of Mechanical Engineering, BAUET
Drawing board
Drawing sheet
T- square
Instrument box containing only compass
Drawing pencils (2H and may have 4H)
Eraser
Adhesive tape
Sharpener
Duster cloth

## Slide 15: Drawing Conventions & Standards
Department of Mechanical Engineering, BAUET
Conventions – commonly accepted practices, rules, or methods
Dashed lines are used to represent hidden features of an
engineering drawing..
Hidden lines – location of drilled hole’s diameter, in a view where the hole cannot be directly seen.

## Slide 16: Drawing Conventions & Standards
Department of Mechanical Engineering, RUET
Standard are a set of rules that governs how technical drawings are represented
Standard are published by organizations with an interest in uniformity
ANSI – American National Standards Institute
    ANSI Y14.1 1980 (R1987) – Drawing sheet size and format
    ANSI Y 14.2M-1979 (R1987) – Line conventions and lettering
    ANSI Y14.5M-1982(R1988) – Dimensioning and tolerances
    ANSI Y 14.3-1975(R1987) – Multi view and sectional view drawings
ISO – International Standards Organization
JIS – Japanese Standards
BIS – Bureau of Indian Standards

## Slide 17: Line Types and Styles
Department of Mechanical Engineering, BAUET

## Slide 18: Line Types and Styles
Department of Mechanical Engineering, BAUET

## Slide 19: Line Types and Styles
Department of Mechanical Engineering, BAUET

## Slide 21: Line Types and Styles
Department of Mechanical Engineering, BAUET

## Slide 22: Line Types and Styles
Department of Mechanical Engineering, BAUET

## Slide 23: Lettering
Department of Mechanical Engineering, BAUET
Freehand Lettering
Developing good lettering is a personal skill which takes practice. Letters must be formed properly.
They must be open shaped very legible.
Clear communication is essential to avoid mistakes and reduce waste.
Lettering may be done using a drafting type pencil, lead holder or technical pen. Which ever tool is used, the letters must properly formed and very black

## Slide 24: Lettering…
Department of Mechanical Engineering, BAUET
Vertical capital letters are preferred for most technical work. They are formed within a 6 by 6 grid.

## Slide 25: Lettering…
Department of Mechanical Engineering, BAUET
Most letters are slightly narrower than they are tall. The shapes of the letters are as open as possible. Letters with small loops and crossing strokes are avoided

## Slide 26: Lettering…
Department of Mechanical Engineering, BAUET
This sequence is recommended to assure that each letter is the correct width in relation in height. For example, form the two vertical sides of the “H”, “N” and “M” first. Form the top of the “T” first.

## Slide 27: Lettering…
Department of Mechanical Engineering, BAUET
The “H” and “N” are slightly narrower than they are tall.
The “T” and the “M” are just as wide as they are tall
Note: Proportion: width vs. height is very important in forming letters.

## Slide 28: Lettering…
Department of Mechanical Engineering, BAUET
Single Stroke Gothic Lettering

## Slide 29: Lettering…
Department of Mechanical Engineering, BAUET
Lettering – Vertical Gothic Font

## Slide 30: Lettering…
Department of Mechanical Engineering, BAUET
Lettering – Vertical Gothic Font

## Slide 31: Lettering…
Department of Mechanical Engineering, BAUET
Lettering with Fractions

## Slide 32: Scales
Department of Mechanical Engineering, BAUET
A scale is defined as the ratio of the linear dimension of the object as represented in a drawing to the actual dimensions of the same.
Scales are used to prepare drawing at:
  Full size
  Reduced size
  Enlarged size

## Slide 33: Layout
Department of Mechanical Engineering, BAUET
inch
TITLE BLOCK
Drawing Sheet
Border Line
JOB TITLE
1 inch
inch
inch

## Slide 34: Layout…
Department of Mechanical Engineering, BAUET
4 inch
3 inch
NAME:
ROLL:
SECTION:
DATE: (C/D); Date
SCALE:
inch
inch

## Slide 35
Question ??