## Slide 1: Chapter-4 Digital Transmission

## Slide 2
Data elements are what we need to send; signal elements are what we can send. Data elements are being carried; signal elements are the carriers.
Ratio, r = Data element/Signal element
Data Element vs Signal Element

## Slide 3
Data Rate
The data rate defines the number of data elements (bits) sent in 1s. The unit is bits per second (bps).
The data rate is sometimes called the bit rate.
Signal Rate
The signal rate is the number of signal elements sent in 1s. The unit is the baud.
The signal rate is sometimes called the pulse rate, the modulation rate, or the baud rate.
Goal of Data Communication
Increase the data rate while decreasing the signal rate.
Increasing the data rate increases the speed of transmission.
Decreasing the signal rate decreases the bandwidth requirement.
Data Rate vs Signal Rate

## Slide 4
Relationship between data rate and signal rate: S = c * N * 1/r baud
Where N is the data rate (bps); c is the case factor, which varies for each case; S is the number of signal elements; and r is the previously defined factor. Here, c=1 worst case, c=0 best case and c=1/2 average case.
Example: A signal is carrying data in which one data element is encoded as one signal element ( r = 1). If the bit rate is 100 kbps, what is the average value of the baud rate if c is between 0 and 1?
Solution: We assume that the average value of c is 1/2 . The baud rate is then
Data Rate vs Signal Rate

## Slide 5
Minimum Bandwidth, Maximum Data Rate, * B * r
Minimum signal rate = Minimum Bandwidth = Maximum Data rate
Example: The maximum data rate of a channel is = 2 * B * (defined by the Nyquist formula). Does this agree with the previous formula for ?
Solution: A signal with L levels actually can carry log2L bits per level. If each level corresponds to one signal element and we assume the average case (c = 1/2), then we have
Note
Although the actual bandwidth of a digital signal is infinite, the effective bandwidth is finite.
Data Rate vs Signal Rate

## Slide 6: Basic Terminologies for Line Coding Scheme
Baseline Wandering
In decoding a digital signal, the receiver calculates a running average of the received signal power (voltage or amplitude).
This average is called the baseline.
The incoming signal power is evaluated against this baseline to determine the value of the data element.
A long string of 0’s or 1’s can cause a drift in the baseline (baseline wandering) and make it difficult for the receiver to decode correctly.

## Slide 7: Basic Terminologies for Line Coding Scheme
Baseline Wandering

## Slide 8: Basic Terminologies for Line Coding Scheme
DC Components Problem
When the voltage level in a digital signal is constant for a while, the spectrum creates very low frequencies.
These frequencies around zero, called DC (direct-current) components.
For example, a telephone line cannot pass frequencies below 200 Hz.

## Slide 9: Basic Terminologies for Line Coding Scheme
Self Synchronization
To correctly interpret the signals received from the sender, the receiver's bit intervals must correspond exactly to the sender's bit intervals.
If the receiver clock is faster or slower, the bit intervals are not matched and the receiver might misinterpret the signals.
A self-synchronizing digital signal includes timing information in the data being transmitted.
This can be achieved if there are transitions in the signal that alert the receiver to the beginning, middle, or end of the pulse.
Notes: If receiver faster than sender than extra bit will be added to the receiver. If receiver is slower than the sender than the receiver might loss some bits.

## Slide 10: Basic Terminologies for Line Coding Scheme
Self Synchronization
Figure: Effect of lack of synchronization

## Slide 11: Basic Terminologies for Line Coding Scheme
Self Synchronization
Example: In a digital transmission, the receiver clock is 0.1 percent faster than the sender clock. How many extra bits per second does the receiver receive if the data rate is 1 kbps? How many if the data rate is 1 Mbps?
Solution:
100 …………… 0.1 extra bit
1………………. (0.1/100) extra bit 1000…………….(0.1/100) * 1000 = 1 extra bit

## Slide 12: Basic Terminologies for Line Coding Scheme
Built-in Error Detection:- It is desirable to have a built-in error-detecting capability in the generated code to detect some of or all the errors that occurred during transmission.
Immunity to Noise and Interference:- Another desirable code characteristic is a code that is immune to noise and other interferences.
Complexity:- A complex scheme is more costly to implement than a simple one. For example, a scheme that uses four signal levels is more difficult to interpret than one that uses only two levels.

## Slide 13: Digital to Digital Conversion
Digital to digital conversion is used to represent digital data in digital signal.
The conversion involves three techniques: line coding, block coding, and scrambling.
Line Coding
Line coding is the process of converting digital data to digital signals.
Line coding converts a sequence of bits to a digital signal.
At the sender, digital data are encoded into a digital signal.
At the receiver, the digital data are recreated by decoding the digital signal.

## Slide 14: Line Coding
Line coding is divided into five categories:-

## Slide 15: Line Coding
Unipolar (Not-Return-to-Zero)
Positive voltage defines bit 1 and the zero voltage defines bit 0.
It is called NRZ because the signal does not return to zero at the middle of the bit.

## Slide 16: Line Coding
Advantages of Unipolar (Not-Return-to-Zero)
Very simple.
Occupies lesser bandwidth.
Disadvantages of Unipolar NRZ
It has DC component problem for 1’s.
It suffers from baseline wandering problem for 1’s.
No error correction done.
No self synchronization.
Greater normalized power.

## Slide 17: Line Coding
Polar (NRZ-L)
The level of voltage determines the values of bit.
Bit 1 Negative Voltage, Bit0 Positive Voltage.
The voltages are on both sides of the time axis.
Polar (NRZ-I)
Change or lack of change in the level of voltage determines the values of bit.
Bit 1 Change, Bit 0No Change.
Let us assume the last voltage level was positive.

## Slide 18: Line Coding
Average Signal Rate:
Here, for average signal rate, the case factor c=1/2 and N=data rate,
Example: A system is using NRZ-I to transfer 1-Mbps data. What are the average signal rate and minimum bandwidth?
Solution: The average signal rate is S= c x N x R = 1/2 x N x 1 = 500 kbaud. The minimum bandwidth for this average baud rate is B(min) = S = 500 kHz.

## Slide 19: Line Coding
Disadvantages of Polar (NRZ-L & NRZ-I):
Baseline wandering problems for long 0’s and long 1’s (NRZ-L).
Baseline wandering problems for long sequence of 0’s (NRZ-I).

## Slide 20: Line Coding
Disadvantages of Polar (NRZ-L & NRZ-I):
Synchronization problem also exists in both NRZ-L and NRZ-I and like before the problem is more severe in NRZ-L.

## Slide 21: Line Coding
Disadvantages of Polar (NRZ-L & NRZ-I):
DC component problems for 0’s and 1’s (NRZ-L).
DC component problems for 0’s (NRZ-I).

## Slide 22: Line Coding
Due to lack of synchronization in NRZ scheme, the receiver does not know when one bit has ended and next bit is starting.

## Slide 23: Line Coding
Polar return to zero scheme solves the problem by marking the middle of the by a transition to zero.

## Slide 24: Line Coding
Polar (Return-to-Zero)
It uses three voltage levels +V, 0 and –V.
Negative voltage represents ‘0’ and positive voltage represents ‘1’.
Always goes to zero at the middle of the bit and stays there until the start of the next bit.
Advantages
There is no DC component problem.
No DC component problem.
Synchronization is possible.
Disadvantages
It uses three level of voltage and complex.
Signal rate is high.

## Slide 25: Line Coding
Polar Bi-phase (Manchester and Differential Manchester)
Manchester coding consists of combining the NRZ-L and RZ schemes.
Differential Manchester coding consists of combining the NRZ-I and RZ schemes. Let us assume last voltage level was positive.

## Slide 26: Line Coding
Advantages
There is no DC component problem.
Synchronization is possible.
There is no baseline wandering problem.
Disadvantages
Signal rate is high.
Note
In Manchester and differential Manchester encoding, the transition
at the middle of the bit is used for synchronization.

## Slide 27: Line Coding
In bipolar encoding (multilevel binary), there are three voltage levels: positive, negative, and zero.
The voltage level for one data element is at zero, while the voltage level for the other element alternates between positive and negative.
It has two types:
1. Alternative Mark Inversion (AMI): For AMI, bit 1 alternate between +V and –V and bit 0Zero Voltage. Let’s assume last non-zero pulse was negative.
2. Pseudo-ternary: For AMI, bit 0 alternate between +V and –V and bit 1Zero Voltage. Let’s assume last zero pulse was negative.

## Slide 28: Line Coding
Advantages
No baseline wandering
No dc component problem
Disadvantages
Synchronization problem
Uses: It is commonly used for long-distance communication.

## Slide 29: Line Coding
Multilevel Schemes
If we have m data elements then we can produce a combination of data patterns.
If we have L different levels, then we can produce combinations of signal patterns.
If < , data patterns occupy only a subset of signal patterns. The subset can be carefully designed to prevent baseline wandering, to provide synchronization, and to detect errors that occurred during data transmission.
Data encoding is not possible if > because some of the data patterns cannot be encoded.
These types of coding can be expressed as mBnL, where m is the length of the binary pattern, B means binary data, n is the length of the signal pattern, and L is the number of levels in the signaling. A letter is often used in place of L: B (binary) for L =2, T (ternary) for L =3, and Q (quaternary) for L =4. Note that the first two letters define the data pattern, and the second two define the signal pattern.

## Slide 30: Line Coding
Multilevel Schemes
2B1Q
In this type of encoding m =2, n =1, and L =4 (quaternary).
Disadvantages:
No self synchronization.
No error detection.
It has dc component problem.
Uses:
2BIQ is used in DSL (Digital Subscriber Line) technology to provide a high-speed connection to the Internet by using subscriber telephone lines.

## Slide 31: Line Coding
2B1Q

## Slide 32: Line Coding
8B6T
Here, 8 bits are used as a pattern of 6 signal elements, where the signal has three levels (ternary). In this type of scheme, we can have 28 =256 different data patterns and 36 =478 different signal patterns.
There are 478 - 256 =222 redundant signal elements that provide synchronization and error detection.
Part of the redundancy is also used to provide DC balance.
Each signal pattern has a weight of 0 or +1 DC values.
This means that there is no pattern with the weight 1.
To make the whole stream Dc-balanced, the sender keeps track of the weight.
If two groups of weight 1 are encountered one after another, the first one is sent as is, while the next one is totally inverted to give a weight of -1.

## Slide 33: Line Coding
8B6T
The three possible signal levels are represented as -,0, and +. The first 8-bit pattern 00010001 is encoded as the signal pattern -0-0++ with weight 0;
The second 8-bit pattern 010 10011 is encoded as - + - + + 0 with weight +1.
The third bit pattern should be encoded as + - - + 0 + with weight +1.
To create DC balance, the sender inverts the actual signal. The receiver can easily recognize that this is an inverted pattern because the weight is -1.
The pattern is inverted before decoding.
The average signal of the scheme theoretically,
In practice, the minimum bandwidth =

## Slide 34: Line Coding
Advantages of 8B6T
No dc component problem.
Synchronization is available.
Error detection available.

## Slide 35: Line Coding
Multiline Transmission (MLT-3)
The multiline transmission, three level (MLT-3) scheme uses three levels (+v, 0, and - V) and three transition rules to move between the levels. 1. If the next bit is 0, there is no transition. 2. If the next bit is 1 and the current level is not 0, the next level is 0. 3. If the next bit is 1 and the current level is 0, the next level is the opposite of the last nonzero level.

## Slide 36: Line Coding
Multiline Transmission (MLT-3)

## Slide 37: Block Coding
Block coding is applied before line coding.
It provides redundancy and improves the performance of line coding.
In general, block coding changes a block of m bits into a block of n bits, where n is larger than m. Block coding is referred to as an mB/nB encoding technique.
It works in three steps: 1. Division 2. Substitution 3. Combination
In the division step, a sequence of bits is divided into groups of m bits.
In the substitution step, it substitutes an m-bit group for an n-bit group.
Finally, the n-bit groups are combined together to form a stream.

## Slide 38: Block Coding

## Slide 39: Block Coding
4B/5B
The four binary/five binary (4B/5B) coding scheme was designed to be used in combination with NRZ-I and solve the synchronization problem of NRZ-I.
It replaces each block of 4 bits with a block of 5 bits has no more than one leading zero (left bit) and no more than two trailing zeros (right bits).
A group of 4 bits can have only 16 different combinations while a group of 5 bits can have 32 different combinations.
This means that there are 16 groups that are not used for 4B/5B encoding.
Some of these unused groups are used for control purposes; the others are not used at all.
The latter provide a kind of error detection. If a 5-bit group arrives that belongs to the unused portion of the table, the receiver knows that there is an error in the transmission.

## Slide 40: Block Coding
4B/5B

## Slide 41: Block Coding
4B/5B Mapping Table

## Slide 42: Block Coding
4B/5B
Disadvantages
It can’t solve the dc component problem of NRZ-I.
It increases the signal rate of NRZ-I.

## Slide 43: Block Coding
8B/10B
A group of 8 bits of data is now substituted by a l0-bit code.
It provides greater error detection capability than 4B/5B. The 8BIlOB block coding is actually a combination of 5B/6B and 3B/4B encoding.
The most five significant bits of a 10-bit block is fed into the 5B/6B encoder; the least 3 significant bits is fed into a 3B/4B encoder.

## Slide 44: Block Coding
8B/10B
To prevent a long run of consecutive 0’s or 1’s, the code uses a disparity controller which keeps track of excess 0’s over 1’s (or 1’s over 0’s).
If the bits in the current block create a disparity that contributes to the previous disparity (either direction), then each bit in the code is complemented (a 0 is changed to a 1 and a 1 is changed to a 0).
The coding has 210 - 28 = 768 redundant groups that can be used for disparity checking and error detection.
In general, the technique is superior to 4B/5B because of better built-in error-checking capability and better synchronization.

## Slide 45: Block Coding
Scrambling
Provide synchronization without increasing the number of bits.
Part of AMI rule is modified to include scrambling.
It is done as same time as line coding.
Two common scrambling techniques are B8ZS and HDB3.

## Slide 46: Block Coding
Scrambling(B8ZS)
It is known as Bipolar with 8 zero substitution.
8 consecutive zeros are substituted by 000VB0VB.
V (violation)- Same as last non-zero level
B(Bipolar)- opposite to last non-zero level

## Slide 47: Block Coding
Scrambling(HDB3)
Four consecutive zero-level voltages are replaced with a sequence of 000V or B00V.
The two rules can be stated as follows: 1. If the number of nonzero pulses after the last substitution is odd, the substitution pattern will be 000V, which makes the total number of nonzero pulses even. 2. If the number of nonzero pulses after the last substitution is even, the substitution pattern will be B00V, which makes the total number of nonzero pulses even.

## Slide 48: Analog to Digital Signal
Digital Data
Digitization
01010101100
Line Coding

## Slide 49: Analog to Digital Signal
Pulse Code Modulation (PCM)
Delta Modulation (DM)

## Slide 50: Analog to Digital Signal
Pulse Code Modulation (PCM):-
It has three steps.
Sampling
Quantizing
Encoding

## Slide 51: Analog to Digital Signal
Pulse Code Modulation (PCM)

## Slide 52: Analog to Digital Signal
Pulse Code Modulation (PCM)
Sampling
Sampling Interval
Sampling rate / frequency,
How many samples are taken in 1s.
This process is also referred as Pulse Amplitude Modulation (PAM)

## Slide 53
Types of Sampling
Natural Sampling
Ideal Sampling
Flat-Top Sampling
Analog to Digital Signal

## Slide 54
Analog to Digital Signal

## Slide 55
Analog to Digital Signal
Nyquist Sampling Theorem
The sampling rate must be at least 2 times the highest frequency contained in the signal.

## Slide 56
Analog to Digital Signal
Nyquist Sampling Theorem

## Slide 57
Analog to Digital Signal
Nyquist Sampling Theorem
Example: A complex low-pass signal has a bandwidth of 200 kHz. What is the minimum sampling rate for this signal?
Solution: The bandwidth of a low-pass signal is between 0 and f, where f is the maximum frequency in the signal. Therefore, we can sample this signal at 2 times the highest frequency (200 kHz). The sampling rate is therefore 400,000 samples per second.
Example: A complex bandpass signal has a bandwidth of 200 kHz. What is the minimum sampling rate for this signal?
Solution: We cannot find the minimum sampling rate in this case because we do not know where the bandwidth starts or ends. We do not know the maximum frequency in the signal.

## Slide 58
Analog to Digital Signal
Sampling
Sampler
Multiply
Message Signal
Impulse Signal
Sampled Signal

## Slide 59
Analog to Digital Signal
Quantization
Message Signal
Sampled Signal
Sampling
Quantizing
Time  Continuous
Amplitude  Continuous
Time  Discrete
Amplitude  Continuous
Time  Discrete
Amplitude  Discrete

## Slide 60
Quantization
Sampling results in a series of pulses of varying amplitude values ranging between two limits: maximum amplitude and minimum amplitude.
The amplitude values are infinite between these two limits.
Quantization process maps these infinite amplitude values onto a finite set of known values.
Analog to Digital Signal

## Slide 61
Steps of Quantization
The original analog signal has amplitude values between and the range is divided into L zones where each of height is delta,
The midpoint of each zone is assigned a value from 0 to L-1 (resulting in L values).
Each sample falling in a zone is then approximated to the value of the midpoint.
Analog to Digital Signal

## Slide 62
Quantization
Analog to Digital Signal

## Slide 63
Quantization Error
Quantization error is the difference between the analog signal and the closest available digital value at each sampling instant.
Quantization error also introduces noise, called quantization noise, to the sample signal which in turn changes the signal to noise ratio.
Analog to Digital Signal

## Slide 64
Quantization Levels
The quantization level mainly depends on-
Analog to Digital Signal
The ranges of amplitudes of the analog signal
How accurate we need to recover the signal

## Slide 65
Transmission Bandwidth
Bit rate =
Bandwidth = c * N * 1/r
= c * * 1/r
If r =1 and c=1/2
Minimum Bandwidth = ½* *
= ½ * * 2 *
= *
If the analog signal is low pass signal then we Bandwidth =
Here, = 0, so bandwidth =
Minimum Bandwidth = *
Analog to Digital Signal

## Slide 66
Delta Modulation (DM)
It builds a second signal that resembles as staircase signal.
Analog to Digital Signal
Step Size,

## Slide 67
Analog to Digital Signal
At each sampling interval, compares the value of the analog signal with the last value of the gradually made staircase signal.
If analog signal > staircase signal  + (+1)
If analog signal < staircase signal - (-0)

## Slide 68
Analog to Digital Signal
If analog signal > staircase signal  + (+1)
If analog signal < staircase signal - (-0)

## Slide 69
Transmission Modes (Digital Transmission)

## Slide 70
Transmission Modes (Digital Transmission)
Parallel Transmission
Use n wires to send n bits at one time.
Advantages
Speed is high, all else being equal, parallel transmission can increase the transfer speed by a factor of n over serial transmission.
Disadvantages
Parallel transmission requires n communication lines. Because this is expensive, parallel transmission is usually limited to short distances.

## Slide 71
Transmission Modes (Digital Transmission)
Serial Transmission
In serial transmission one bit follows another, so we need only one communication channel rather than n to transmit data between two communicating devices.

## Slide 72
Transmission Modes (Digital Transmission)
Advantages of Serial Transmission
The advantage of serial over parallel transmission is that with only one communication channel, serial transmission reduces the cost of transmission over parallel by roughly a factor of n.
Disadvantages of Serial Transmission
Speed comparatively slower than parallel transmission.

## Slide 73
Transmission Modes (Digital Transmission)
Asynchronous Transmission
The timing of a signal is unimportant.
Instead, information is received and translated by agreed upon patterns. As long as those patterns are followed, the receiving device can retrieve the information without regard to the rhythm in which it is sent.
In asynchronous transmission, we send 1 start bit (0) at the beginning and 1 or more stop bits (Is) at the end of each byte. There may be a gap between each byte.
The start and stop bits and the gap alert the receiver to the beginning and end of each byte and allow it to synchronize with the data stream.

## Slide 74
Transmission Modes (Digital Transmission)
Asynchronous Transmission
Advantages
But it is cheap and effective, two advantages that make it an attractive choice for situations such as low-speed communication.
Uses
For example, the connection of a keyboard to a computer is a natural application for asynchronous transmission.

## Slide 75
Transmission Modes (Digital Transmission)
Synchronous Transmission
In synchronous transmission, we send bits one after another without start or stop bits or gaps. It is the responsibility of the receiver to group the bits.
Timing becomes very important, therefore, because the accuracy of the received information is completely dependent on the ability of the receiving device.
The advantage of synchronous transmission is speed. With no extra bits or gaps to introduce at the sending end and remove at the receiving end, and, by extension, with fewer bits to move across the link, synchronous transmission is faster than asynchronous transmission.
For this reason, it is more useful for high-speed applications such as the transmission of data from one computer to another. Byte synchronization is accomplished in the data link layer.

## Slide 76
Transmission Modes (Digital Transmission)
Isochronous Transmission
In real-time audio and video, in which uneven delays between frames are not acceptable, synchronous transmission fails.
For example, TV images are broadcast at the rate of 30 images per second; they must be viewed at the same rate.
If each image is sent by using one or more frames, there should be no delays between frames.
For this type of application, synchronization between characters is not enough; the entire stream of bits must be synchronized. The isochronous transmission guarantees that the data arrive at a fixed rate.